| OEM Front - 245/40R18 >Search Tires | OEM Rear - 265/40R19 >Search Tires |
| --- | --- |
| Section Width: 9.64 in 245 mm | Section Width: 10.43 in 265 mm |
| Rim Diameter: 18 in 457.2 mm | Rim Diameter: 19 in 482.6 mm |
| Rim Width Range: 8 - 9.5 in | Rim Width Range: Unrecognized tire size. |
| Overall Diameter: 25.71 in 653.03 mm | Overall Diameter: 27.34 in 694.43 mm |
| Sidewall Height: 3.85 in 97.79 mm | Sidewall Height: 4.17 in 105.91 mm |
| Radius: 12.85 in 326.39 mm | Radius: 13.67 in 347.21 mm |
| Circumference: 80.77 in 2051.5 mm | Circumference: 85.89 in 2181.6 mm |
| Revs per Mile: 809.0 | Revs per Mile: 760.7 |
| Actual Speed: 60 mph 100 km/h | Speedometer1: 56.4 mph 94.0 km/h |
| Speedometer Difference: - | Speedometer Difference: 6.349% too slow |
| Diameter Difference: - | Diameter Difference: 5.97% |

| TE37 Front - 245/35R19 | TE37 Rear - 285/30R19 >Search Tires |
| --- | --- |
| Section Width: 9.64 in 245 mm | Section Width: 11.22 in 285 mm |
| Rim Diameter: 19 in 482.6 mm | Rim Diameter: 19 in 482.6 mm |
| Rim Width Range: 8 - 9.5 in | Rim Width Range: 10 - 11 in |
| Overall Diameter: 25.75 in 654.05 mm | Overall Diameter: 25.73 in 653.54 mm |
| Sidewall Height: 3.37 in 85.598 mm | Sidewall Height: 3.36 in 85.344 mm |
| Radius: 12.87 in 326.89 mm | Radius: 12.86 in 326.64 mm |
| Circumference: 80.89 in 2054.6 mm | Circumference: 80.83 in 2053.0 mm |
| Revs per Mile: 807.7 | Revs per Mile: 808.3 |
| Actual Speed: 60 mph 100 km/h | Speedometer1: 60.0 mph 100. km/h |
| Speedometer Difference: - | Speedometer Difference: 0.074% too fast |
| Diameter Difference: - | Diameter Difference: 0.08% |